## Slide 1: RISC-V on NIXPKGS
Porting NixOS to the SpacemiT K1 and K3, and making riscv64 usable in nixpkgs
liberodark

## Slide 2: Self presentation
liberodark
IT architect, specialized on Linux
Just another NixOS contributor, since 2023
I also have been working on RISC-V for a few years now
github.com/liberodark

## Slide 3: Why NixOS on RISC-V?
Reproducible builds. The same nixpkgs revision gives the same result on every machine.
Native builds on real hardware. My riscv64 packages are built and tested directly on K3 boards, not cross-compiled.
Hardware support is declarative. Kernel, patches and device tree live in one nixos-hardware module.
One fix unblocks many packages. A fix merged in nixpkgs unblocks everything that depends on it. My builders share their binary caches, so servers can deploy riscv64 applications without rebuilding anything.

## Slide 4: How it began
I started porting NixOS to the SpacemiT K1, then moved to the SpacemiT K3.
After porting the K3 with the vendor kernel (SpacemiT), I successfully brought it to the mainline kernel.
To do so, I had to create custom patches that did not exist yet.
nixos-hardware: modules for the K3 and its variants.

## Slide 5: From K1 to K3: why it matters
 | SpacemiT K1 | SpacemiT K3
CPU | 8 × X60, 1.6 GHz | 8 × X100, 2.4 GHz
ISA profile | RVA22 | RVA23
Memory | up to 16 GB LPDDR4X | up to 32 GB LPDDR5
Storage / I/O | PCIe 2.1 | PCIe Gen3, NVMe, UFS, 10 GbE
Virtualization | no | yes
Why the K3 for NixOS?
• RVA23 is the profile the RISC-V ecosystem now targets. Ubuntu uses RVA23 as its baseline since 25.10, and Ubuntu 26.04 LTS officially supports the K3.
• Native builds: big packages (GHC, .NET, Node.js) can be built and tested on the board. The 32 GB version is needed: 8 or 16 GB is not enough for builds such as Node.js.
• Virtualization: the hypervisor extension (RVH) makes KVM and libkrun possible.

## Slide 6: And now: riscv64 in nixpkgs
Languages & runtimes
.NET 8 / 9 / 10 #557475
GHC 9.6.6 #549823
Dart #555733
Deno #533574
Node.js 22 #555658
Node.js 24 #539503
Temurin (Java) #554603
Gradle #550010
+ pdfium, ffmpeg, schroedinger, httpcore, PostgreSQL…
Infrastructure
Proxmox VE (proxmox-nixos) #248
GitLab #565242
Ceph 20.2 #560645
libkrun #545448
CRIU #545342
BIND #551604
Libraries
libgcrypt #542494
ANGLE #540665
NumPy #523194

## Slide 7: Builders, Hydra and binary caches
3 RISC-V builders on SpacemiT K3, running NixOS: build05, build06, build07.ynh.ovh
Configuration: github.com/liberodark/nix-community-builder
My Hydra instance builds riscv64 packages on these machines
Each builder serves its Nix store as a binary cache over HTTPS (Harmonia)
To use them, in your NixOS configuration:
  nix.settings = {
  substituters = [
  "https://build05.ynh.ovh" "https://build06.ynh.ovh" "https://build07.ynh.ovh"
  ];
  trusted-public-keys = [
  "build05.ynh.ovh:bLxWKPjbKYOFxqrjOxv+cdwS3kFLuHEf1k6j8fAxbzM="
  "build06.ynh.ovh:bPg6x17ztNd3uMxdclDvdJpTl2pwLiTdHTt9ymTNoMU="
  "build07.ynh.ovh:+FpUDKUYk4H9uzLgtbE0MHOx+5Nm7YEFBrJJGiQ9O8U="
  ];
  };

## Slide 8: Goals and what's next
Make NixOS 26.05 and 26.11 usable on RISC-V
nixos-hardware support for the K3 and its variants
Improve evaluation in nixpkgs in general
Next architecture: loongarch64, once riscv64 is done

## Slide 9: Special thanks to...
Gaétan Lepage for supporting my work github.com/GaetanLepage
Mic92 for the PR reviews github.com/Mic92
Wegank for the PR reviews github.com/Wegank
Colemickens for the hardware tests github.com/Colemickens
wolfgangwalther for the GHC part github.com/wolfgangwalther
corngood for the help on .NET github.com/corngood